## Slide 1
An Efficient RFID Tag Estimation Method Using Biased Chebyshev Inequality for Dynamic Frame Slotted ALOHA
Presented by: Hazem Elsaid

## Slide 2: Agenda
Hazem.a.elsaid@fau.de
  Introduction
  Motivation
  Proposed Biased Chebyshev Tag Estimation
  Conclusion

## Slide 3: Agenda
Hazem.a.elsaid@fau.de
  Introduction
  Motivation
  Proposed Biased Chebyshev Tag Estimation
  Conclusion

## Slide 4: Introduction
Radio Frequency Identification (RFID) is a wireless data capture technology that can be used to electronically identify and track objects
Hazem.a.elsaid@fau.de

## Slide 5: Introduction
Bill of Lading
Material Tracking
Wireless
Item Tracking
Shipping Portals
Inventory Management
and Control
RFID applications
Hazem.a.elsaid@fau.de

## Slide 6: Introduction
RFID versus Barcodes:
 | Barcodes | RFID
Advantages | Smaller Cheaper than RFID Higher accurecy (today) | Large reading distance. Non-LOS technology. Automatic reading process. More secure (kill, password) Reusable. Higher reading rate.
Disadvantages | LOS technology. Small reading distance. Indvidual scanned. Easily damaged | Tag collision (dense network). Reader collision.
Hazem.a.elsaid@fau.de

## Slide 7: Introduction
RFID Components
Hazem.a.elsaid@fau.de

## Slide 8: Introduction
RFID operating frequencies and its specifications
Microwave | Ultra High Frequency (UHF) | High Frequency (HF) | Low Frequency (LF) | 
2.45-5.8 GHz | 860-960 MHz | 13.56 MHz | 126-134 KHz | Frequency Range
5-100m | 2-10m | 1m | 10cm | Read Range
Electro magnetic | Electro magnetic | Magnetic | Magnetic | Coupling
18000-4 | EPC C0, C1, C1G2, 18000-6 | 18000-3.1, 15693,14443 A, B, and C | 11784/85, 14223 | Existing standards
Hazem.a.elsaid@fau.de

## Slide 9: Introduction
RFID operating frequencies and its specifications
Microwave | Ultra High Frequency (UHF) | High Frequency (HF) | Low Frequency (LF) | 
2.45-5.8 GHz | 860-960 MHz | 13.56 MHz | 126-134 KHz | Frequency Range
5-100m | 2-10m | 1m | 10cm | Read Range
Electro magnetic | Electro magnetic | Magnetic | Magnetic | Coupling
18000-4 | EPC C0, C1, C1G2, 18000-6 | 18000-3.1, 15693,14443 A, B, and C | 11784/85, 14223 | Existing standards
Hazem.a.elsaid@fau.de

## Slide 10: Introduction
Types of tags in RFID Systems
 | Active Tags | Passive Tags
Tag Power Source | Internal to the tag | Transferred from reader using RF signal
Tag Battery | Yes | No
Avilability of Power | Continious | In reading range
Required Signal strength | Very low | Very high
Reading range | Up to 100 m | Up to 10 m
Hazem.a.elsaid@fau.de

## Slide 11: Introduction
Types of tags in RFID Systems
 | Active Tags | Passive Tags
Tag Power Source | Internal to the tag | Transferred from reader using RF signal
Tag Battery | Yes | No
Avilability of Power | Continious | In reading range
Required Signal strength | Very low | Very high
Reading range | Up to 100 m | Up to 10 m
Hazem.a.elsaid@fau.de

## Slide 12: Agenda
Hazem.a.elsaid@fau.de
  Introduction
  Motivation
  Proposed Biased Chebyshev Tag Estimation
  Conclusion

## Slide 13: Motivation
Single Reader Vs. multiple passive tags.
Reader
Tag
Interrogation Zone
Hazem.a.elsaid@fau.de

## Slide 14: Motivation
Single Reader Vs. multiple passive tags.
Reader
Tag
Interrogation Zone
Successful
Hazem.a.elsaid@fau.de

## Slide 15: Motivation
Single Reader Vs. multiple passive tags.
Reader
Tag
Interrogation Zone
No Answer
Hazem.a.elsaid@fau.de

## Slide 16: Motivation
Single Reader Vs. multiple passive tags.
Collision Problem.
Reader
Tag
Interrogation Zone
Multiple answer
Hazem.a.elsaid@fau.de

## Slide 17: Motivation
  Time is divided into equally sized frames, each tag can access only one slot per frame.
Frame Slotted ALOHA
  Number of idle slots:
  Number of Successful slots:
  Number of collided slots:
Where:
n: Number of Tags
L: Frame Length
Hazem.a.elsaid@fau.de

## Slide 18: Motivation
Frame Slotted ALOHA
  Reading efficiency
  For maximum reading efficiency:
  n is unknown ???
Hazem.a.elsaid@fau.de

## Slide 19: Agenda
Hazem.a.elsaid@fau.de
  Introduction
  Motivation
  Proposed Biased Chebyshev Tag Estimation
  Conclusion

## Slide 20: Proposed Biased Chebyshev Tag Estimation
Classical Chebyshev Inequality Tag Estimation
Where:
- L is the frame length.
- n is the number of tags to be estimated.
- k is a constant >1.
Number of idle, successful, collided slots form the last reading cycle
Hazem.a.elsaid@fau.de

## Slide 21: Proposed Biased Chebyshev Tag Estimation
Collision Coefficient
Hazem.a.elsaid@fau.de
n >> L
n << L
n ≈ L
Frame Length= 512

## Slide 22: Proposed Biased Chebyshev Tag Estimation
Two dimensional Curve fitting:
Hazem.a.elsaid@fau.de
L | Collision Coefficient
20 | X0
21 | X1
215 | X15
First dimension is L:
Second dimension is n:
Proposed collision coefficient equation

## Slide 23: Proposed Biased Chebyshev Tag Estimation
Hazem.a.elsaid@fau.de

## Slide 24: Proposed Biased Chebyshev Anti-collision Algorithm
Hazem.a.elsaid@fau.de
Set initial frame length =128
Observe:
Collided Slots
Successful Slots
Empty Slots
Collided & Successful =0
Calculate:
Collision coefficient
Estimated number of tags
Frame length
End

## Slide 25: Proposed Biased Chebyshev Anti-collision Algorithm
Saving of time using the proposed biased Chebyshev estimation w.r.t. the classical Chebyshev:
Hazem.a.elsaid@fau.de

## Slide 26: Agenda
Hazem.a.elsaid@fau.de
  Introduction
  Motivation
  Proposed Biased Chebyshev Tag Estimation
  Conclusion

## Slide 27: Conclusion
Hazem.a.elsaid@fau.de

## Slide 28
Thanks for your attention