## Slide 1
FFT Based Rate Estimation for UHF RFID Systems
Hamed Salah
Smart SysTech 2015, 17.06.2015

## Slide 2: Motivation
RFID is an non line of sight (NLOS) identification technology
RFID system contains tags and reader.
Frame slotted Aloha (FSA) is used as an anti-collision algorithm
The reader tells the tags about the frame length and each tag selects a slot randomly to transmit its ID in it.
Collision might be happened
Notes: How can we estimate the rate of the strongest tag

## Slide 3: Motivation
Converting collided slots into successful slots to increase the throughput per frame
C2 , C3 , and C4 are 2, 3, and 4 tags collided slots the throughput per frame = 42.9%
Only the strongest tag is recovered for each
collided slot, the throughput per frame= 85.7%
Only single tag is recovered for each collided slot
To decode the strongest tag reply, its symbol duration (symbol rate) has to be accurately known
How can we estimate the rate of the strongest tag
S: Successful slot
              C: Collided slot
E: Empty slot
Notes: How can we estimate the rate of the strongest tag

## Slide 4: Agenda
Rate Tolerance Problem
FFT Based Rate Estimation for Collided Tags
Results and Simulations
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 5: Rate Tolerance Problem
One of the most RFID challenging problems is the tolerance in the rate of the tag reply which is called Backscatter Link Frequency (BLF)
Reasons of rate tolerance:
  Error in measuring the Tag to Reader Calibration signal (TRcal)
  Manufacturing process variations.
In single tag reply, multiple correlators are used to estimate the BLF
In Collided slots, the time domain solution is not suitable for BLF estimation
Tx
Rx
RFID Reader
Tag
Measuring TRcal
Calculating the symbol rate
Estimate the symbol rate
Decode the tag
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 6: Rate Tolerance Problem
Tag to Reader Encoding
Notes: Headline FM0 Encoding scheme

## Slide 7: Rate Tolerance Problem
Tag to Reader Encoding
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 8: Rate Tolerance Problem
The Tag uses the Divide Ratio (DR), TRcal, Type of encoding scheme to calculate the symbol rate
DR: Divide Ratio | BLF: Link Frequency(kHz) | Frequency Tolerance FT
64/3 | 640 | +/-15%
 | 320<BLF<640 | +/-22%
 | 320 | +/-10%
 | 256<BLF<320 | +/-12%
8 | 320 | +/-10%
 | 256<BLF<320 | +/-12%
 | 160 | +/-7%
 | 40<BLF<107 | +/-4%
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 9: Agenda
Rate Tolerance Problem
FFT Based Rate Estimation for Collided Tags
Results and Simulations
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 10: FFT Based Rate Estimation for Collided Tags
  System Model
  xi is tag reply encoded either with FM0 or Miller
  j is the number of collided tags, it can be 1 (single tag reply), 2, 3, or 4 for collided slots
  The magnitude of hi is backscatter Rayleigh channel
  n(t) is zero mean AWGN
Calculation of
percentage of failure
Strongest tag rate estimation
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 11: FFT Based Rate Estimation for Collided Tags
Single tag rate estimation with FM0
  FFT is used with the preamble pilot tone to get the rate of the strongest tag
Tag ID
Tag preamble
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 12: FFT Based Rate Estimation for Collided Tags
Single tag rate estimation with FM0
  FFT is used with the preamble pilot tone to get the rate of the strongest tag
  The nominal value of the
  rate equals to 640 kHz,
  there is a tolerance with
  3.9%
  The symbol rate = BLF
Tag ID
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 13: FFT Based Rate Estimation for Collided Tags
Single tag rate estimation with Miller
  The preamble will be longer and equals to 16*M, where M=2, 4, 8
  The nominal value of the
  rate equals to 640 kHz,
  there is a tolerance with
  -3.87%
  The symbol rate = BLF/M
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 14: FFT Based Rate Estimation for Collided Tags
Strongest tag rate estimation with FM0
  Two tags reply with nominal rate=640 kHz, however they reply with two different rates, 623 kHz and 727 kHz with tolerance -2.66% and 13.6% respectively
The strongest tag
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 15: FFT Based Rate Estimation for Collided Tags
Strongest tag rate estimation with Miller
  Three tags reply with nominal rate=640 kHz, however they reply with three different rates, 571 kHz, 616 kHz, and 667 kHz with tolerance -10.78%, -3.75%, and 4.22 respectively
The strongest tag
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 16: Agenda
Rate Tolerance Problem
FFT Based Rate Estimation for Collided Tags
Results and Simulations
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 17: Results and Simulations
Rate estimation comparison between 4 different BLFs for single tag with FM0
  The nominal values for BLF=640, 256, 160, 40 kHz, fs=8 MSps, and the tolerance is normal distribution with zero mean and variance according to the standard
  The Percentage of Failure (PoF) is used as performance metric
  The failure happens when the error in estimation causes a shift by more than half symbol at the end of tag reply.
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 18: Results and Simulations
Rate estimation comparison between FM0 and Miller (M=2, 4, 8) for single tag
  The nominal BLF=640 kHz, fs=8 MSps, and the tolerance is normal distribution with zero mean and variance according to the standard
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 19: Results and Simulations
Rate estimation comparison between 2, 3, and 4 collided tags with FM0
  The nominal BLF=640 kHz, fs=8 MSps, and the tolerance is normal distribution with zero mean and variance according to the standard
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 20: Results and Simulations
Rate estimation for 2, 3, and 4 collided tags with Miller and M=8
  The nominal BLF=640 kHz, fs=8 MSps, and the tolerance is normal distribution with zero mean and variance according to the standard
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 21: Conclusion
Rate estimation in RFID is a crucial issue while doing collision recovery
Time domain solution (multiple correlators) is used to estimate the rate of single tag reply
In collided slots, the multiple correlators fail to estimate the BLF of any of collided tags.
The Frequency domain is utilized to estimate the BLF of the strongest tag reply either in successful slot or in collided slot
The FFT is used to estimate the BLF of the Tag reply
  The FFT is used to estimate the BLF of the tag reply in successful slot with different rates
  The lower rates give lower PoF than the higher rates
  The performance is tested when the tag uses FM0 and Miller as an encoding technique.
  Miller gives better performance from BLF estimation point of view. However, the symbol rate is decreased
  The performance is tested for collided slots with 2, 3, and 4 collided tags
  The PoF saturates with the SNR for 3 and 4 collided tags because the effect of the interference is more dominant than the effect of noise
Notes: Focus; no traffic from BS to node;
When sensor node tries to communicate with the BS, we‘ll definitely face performance degradation;
there will be some ambient noise, for example caused by receiver electronics; usually modelled as AWGN; not the focus here
Limiting factor…; to quantify or even mitigate interference effects, appropriate/accurate interference models are required
Aim: present an interference modelling approach; …
capture effect: The stronger signal wins; Verknüpfung untere und obere Abbildung

## Slide 22
Thanks for your kind attention!
hamed.kenawy@fau.de