## Slide 1
An Efficient RFID Tag Estimation Method Using Biased Chebyshev Inequality for Dynamic Frame Slotted ALOHA
Hazem Elsaid
Smart SysTech 2014, 02.07.2014

## Slide 2: Agenda
Motivation
Classical Tag Estimation Methods
Proposed Biased Chebyshev Tag Estimation
Conclusion and Future Work
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 3: Motivation
System Model:
  Single RFID Reader.
  Dense RFID network with unknown number
  of passive tags.
  Tags should be identified in the minimum
  possible time.

## Slide 4: Motivation
System Model:
  Single RFID Reader.
  Dense RFID network with unknown number
  of passive tags.
  Tags should be identified in the minimum
  possible time.
Identification Process:
  Reader asks the tags for there EPC code.

## Slide 5: Motivation
System Model:
  Single RFID Reader.
  Dense RFID network with unknown number
  of passive tags.
  Tags should be identified in the minimum
  possible time.
Identification Process:
  Reader asks the tags for there EPC code.
  Single answer (Successful).

## Slide 6: Motivation
System Model:
  Single RFID Reader.
  Dense RFID network with unknown number
  of passive tags.
  Tags should be identified in the minimum
  possible time.
Identification Process:
  Reader asks the tags for there EPC code.
  Single answer (Successful).
  No answer.

## Slide 7: Motivation
System Model:
  Single RFID Reader.
  Dense RFID network with unknown number
  of passive tags.
  Tags should be identified in the minimum
  possible time.
Identification Process:
  Reader asks the tags for there EPC code.
  Single answer (Successful).
  No answer.
  Multiple answers. (Collision)
What is the maximum achievable identification efficiency?

## Slide 8: Motivation
Dynamic Framed Slotted ALOHA:
  Time divided into multiple frames.
  Each frame has different length (number of slots).
  Reader has to inform the tags with the frame size (Q value).
  Each tag chooses only one random slot per frame.
Maximum reading efficiency:
Frame1
Frame2
Framei
Total reading time
S2Q-1
S1
S2
S3
L
Where:
- Collided Slot
- Successful Slot
- Idle Slot
Robust number of tags estimation
Unknown number of tags
n=?

## Slide 9: Motivation
Complete anti-collision algorithm:
Set initial frame length
Observe:
Collided Slots
Successful Slots
Empty Slots
Collided & Successful slots =0
Estimated number of tags (n)
Calculate the new optimum frame length (L)
End
yes
No

## Slide 10: Motivation
Complete anti-collision algorithm:
Set initial frame length
Observe:
Collided Slots
Successful Slots
Empty Slots
Collided & Successful slots =0
Estimated number of tags (n)
Calculate the new optimum frame length (L)
End
yes
No

## Slide 11: Agenda
Motivation
Classical Tag Estimation Methods
Proposed Biased Chebyshev Tag Estimation
Conclusion and Future Work

## Slide 12: Classical Tag Estimation Methods
Lower bound:
  Assumes two tags collided per collided slot (Lower bound of collision).
Schoute:
  Assumes Poisson distribution, then calculates the expected number of collisions per slot.
 Both these methods depends only on one information (number of collided slots)

## Slide 13: Classical Tag Estimation Methods
Classical Chebyshev Tag estimation methods
Messured number of idle, successful, collided slots
Expected number of idle, successful, collided slots
Idle
Successful
Collided

## Slide 14: Classical Tag Estimation Methods
Estimation error for the classical tag estimation methods
  Frame length L=128.
  Classical Chebyshev is the most promising tag estimation method.
  The estimation error increase when the actual number of tags increases.

## Slide 15: Agenda
Motivation
Classical Tag Estimation Methods
Proposed Biased Chebyshev Tag Estimation
Conclusion and Future Work

## Slide 16: Proposed Biased Chebyshev Tag Estimation
Classical Chebyshev Tag estimation :
Numerical example:
  |a0-c0|= k  error = k tags.
  |a1-c1|= k  error = k tags.
  |ak-ck|= k  error ≥ 2*k tags. (depends on the existing number of tags).
Proposed biased Chebyshev Tag estimation:
Collision Coefficient

## Slide 17: Proposed Biased Chebyshev Tag Estimation
Estimation error curve:
  Frame length L=512
  Number of tags >> L Number of collided slots is dominant.
  Number of tags << L Number of collided slots is very small.
  L/2< Number of tags <2L  Variable collision coefficient ( ) for minimum estimation error.
Using simulations the proposed collision coefficient equation:

## Slide 18: Proposed Biased Chebyshev Tag Estimation
Estimation error for the proposed tag estimation compared to the classical methods:
  Frame length L=128
  The proposed collision coefficient compensates the increase of the mean estimation error with the increase of the number of tags.

## Slide 19: Proposed Biased Chebyshev Tag Estimation
Percentage of saving time using the proposed algorithm compared to the classical Chebyshev algorithm:
  Starting frame length L=128
  Oscillations in the curve are due to the frame length takes only discrete values 2Q.
  Negative value at with a tag populations less than 25 tags has a very small effect.

## Slide 20: Agenda
Motivation
Classical Tag Estimation Methods
Proposed Biased Chebyshev Tag Estimation
Conclusion and Future Work

## Slide 21: Conclusion and future work
Conclusion
  A new biased Chebyshev inequality tag estimation method is proposed.
  The proposed method is compared with the classical tag estimation methods and gives better results with dense RFID networks.
  A new biased Chebyshev inequality anti-collision algorithm is presented.
  The new algorithm compared with the classical Chebyshev inequality anti-collision and the reading time is reduced by 25%.
Future work
  The successful and empty coefficients should be also calculated and added to the main estimation equation.
  Compare the new estimation performance with the current performance in terms of estimation error and saving time.
Notes: straight forward evaluation
easy consideration of different propagation channels
typical nodes suffer from frequency offset etc. -> requires advanced modelling

## Slide 22
Thanks for your kind attention!
Hazem.a.elsaid@fau.de