## Slide 1
Backwards Compatible Improvement of the
EPCglobal Class 1 Gen 2 Standard
Hazem A. Ahmed
IEEE RFID-TA 2015, 18.09.2015

## Slide 2: Motivation
System Model:
  Single RFID reader.
  Dense RFID network >3000 passive UHF tags.
  Working standard EPCglobal C1 G2 with Framed Slotted ALOHA anti-collision protocol.
  Tags should be identified in the minimum possible time.
http://bin95.com/BarCode_RFID.htm

## Slide 3: Motivation
Conventional Framed Slotted ALOHA
  No collision recovery capability
  C2 , C3 , and C4 are 2, 3, and 4 tags collided slots
Improved Framed Slotted ALOHA with Collision Recovery
  Convert part of the collided slots into successful slots
  Acknowledge only one tag per collided slot (EPCgloabal C1G2).
S
C2
E
S
C3
E
C4
S
S
E
S
S
E
S
S
C2
E
S
C3
E
C4
Can we Acknowledge more than one tag per slot under EPCglobal C1G2?
S: Successful slot
C: Collided slot
E: Empty slot

## Slide 4: Agenda
EPCglobal C1 G2 Reading Process
Proposed System Description
  Proposed Tags
  Proposed Reader
Performance Analysis
Measurements and Simulation Results
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 5: EPCglobal C1 G2 Reading Process
L
Reader
Tag
Interrogation Zone

## Slide 6: EPCglobal C1 G2 Reading Process
E
L
Reader
Tag
No Answer

## Slide 7: EPCglobal C1 G2 Reading Process
E
C
L
Reader
Tag
Multiple answer

## Slide 8: EPCglobal C1 G2 Reading Process
E
S
C
L
Reader
Tag
Unique answer

## Slide 9: EPCglobal C1 G2 Reading Process
E
S
C
L
1
Reader
Tag
2
Collision Recovery
1
2

## Slide 10: EPCglobal C1 G2 Reading Process
E
S
C
L
1
Reader
Tag
2
1
2
ACK
1
2
2
2
RN162
Arbitrate State
ACK State

## Slide 11: EPCglobal C1 G2 Reading Process
E
S
C
L
Reader
Tag
2
1
2
1
2
2
2
EPC2

## Slide 12: Agenda
EPCglobal C1 G2 Reading Process
Proposed System Description
  Proposed Tags
  Proposed Reader
Performance Analysis
Measurements and Simulation Results
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 13: Proposed System Description (Tag)
Properties of the proposed Tag:
  It includes two modes:
    Conventional mode (default)
    Modified mode (when it receives switch command)
  The Pilot is divided into:
    4-bits zeros for synchronization
    8-bits orthogonal pilots for channel estimation
P1 | 1 -1 1 -1 1 -1 1 -1 1 -1 1 -1 1 -1 1 -1
P18 | 1 -1 1 -1 1 -1 1 1 -1 1 -1 1 -1 1 -1 -1
P69 | 1 -1 1 1 -1 1 -1 1 -1 1 -1 -1 1 -1 1 -1
P86 | 1 -1 1 1 -1 1 -1 -1 1 -1 1 1 -1 1 -1 -1
P171 | 1 1 -1 1 -1 -1 1 -1 1 1 -1 1 -1 -1 1 -1
P188 | 1 1 -1 1 -1 -1 1 1 -1 -1 1 -1 1 1 -1 -1
P239 | 1 1 -1 -1 1 1 -1 1 -1 -1 1 1 -1 -1 1 -1
P256 | 1 1 -1 -1 1 1 -1 -1 1 1 -1 -1 1 1 -1 -1
Example for the 8-bits orthogonal pilot [J. Kaitovic 2012]
a- Conventional tag reply
b- Proposed tag reply

## Slide 14: Proposed System Description (Tag)
Properties of the proposed Tag:
  It includes two modes:
    Conventional mode (default)
    Modified mode (when it receives switch command)
  The Pilot is divided into:
    4-bits zeros for synchronization
    8-bits orthogonal pilots for channel estimation
  Wait state is defined for the proposed tag, in this state:
    Tag enters this state when it receives ACK command with invalid RN16.
    Tag keeps on its RN16 value and wait for valid ACK to enter the Acknowledged state.
    Tag goes to Arbitrate state when:
      The waiting time proceeds the time out.
      It receives any command except ACK command.

## Slide 15: Proposed System Description (Reader)
Properties of the proposed reader:
  Switch command is transmitted at the beginning of the inventory round
  Converts the collided slot into pseudo parallel slot
  Counts the number of single reply from each orthogonal pilot
  Extracts each RN16 corresponding to each single pilot reply
  Sends successive ACK commands until finishing all the extracted RN16s.
  recognizes if one of these replies is the conventional pilot or not:
    If yes, acknowledges the conventional tag first.
    If no, start from the weakest reply to the strongest.
 | Switch Command
Number of bits | 16
Description | 1110001001100000
Proposed switch command

## Slide 16: Agenda
EPCglobal C1 G2 Reading Process
Proposed System Description
  Proposed Tags
  Proposed Reader
Performance Analysis
Measurements and Simulation Results
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 17: Performance Analysis
New Reading Process
  Each color presents tags with a unique and orthogonal
  pilot.
  The blue color presents conventional tag with
  the conventional pilot.
Reader
Conventional Tag
New Tag

## Slide 18: Performance Analysis
New Reading Process
3
2
1
Reader
Conventional Tag
New Tag
RN162
RN163
RN161
E
S
C
RN161
RN162
RN163
Pilot1
8 bits
16 bits
Pilot2
Pilot3

## Slide 19: Performance Analysis
New Reading Process
3
2
1
Reader
Conventional Tag
New Tag
E
S
C
Pseudo parallel successful slot
ACK3+
EPC
ACK1
+EPC
ACK2
+EPC
Query
+ RN16s
Conventional tag
ACK2
ACK3
ACK1

## Slide 20: Performance Analysis
Proposed pseudo parallel slot duration
S
E
C
ACK+EPC
Query
+ RN16
30%
70%
ACK1+
EPC
ACKRsol
+EPC
Query
+ RN16

## Slide 21: Performance Analysis
Proposed Reading Efficiency :
,
Where:
  is the probability that exactly R tags are active in one slot, .
  is the maximum number of tags that can be resolved. In our case (.
  presents the number of recovered tags
  represents the probability that scenario happens [J. Kaitovic 2013].
  is the pseudo parallel factor
Number of replied tags | Probability of unique scenario
1 | 
(1+1) | 0.875
(1+1+1) | 
(1+1+1+1) | 
(1+1+1+1+1) | 
(1+1+1+1+1+1) | 
(1+1+1+1+1+1+1) | 
(1+1+1+1+1+1+1+1) | 
 | Probability of unique scenario
1 | 
(1+1) | 
(1+1+1) | 
(1+1+1+1) | 
(1+1+1+1+1) | 
(1+1+1+1+1+1) | 
(1+1+1+1+1+1+1) | 
(1+1+1+1+1+1+1+1) | 

## Slide 22: Agenda
EPCglobal C1 G2 Reading Process
Proposed System Description
  Proposed Tags
  Proposed Reader
Performance Analysis
Measurements and Simulation Results
Conclusion
Notes: presentation consists of 5 parts
based on NW, we‘ll model the interference seen by the base station
I‘ll close with some conlcusions

## Slide 23: Measurements and Simulation Results
Communication link measurement:
  The proposed reader is implemented on USRP B210.

## Slide 24: Measurements and Simulation Results
Measurements Equipment:
  The proposed tag is implemented on WISP 5.0.

## Slide 25: Measurements and Simulation Results
Reading Efficiency comparison:
  We used in simulations 8 orthogonal pilots
  Fully parallel tags acknowledgment not applicable in practice.

## Slide 26: Measurements and Simulation Results
Average reading time comparison:
  C. Angerer [5] recover all the two collided tags.
  J. Kaitovic [6] uses 8 orthogonal preambles but acknowledge only single tag.
  The proposed system used the orthogonal pilots and the pseudo parallel acknowledgment.

## Slide 27: Conclusion
A new RFID system (Readers and Tgas) compatible with UHF EPCglobal class 1 gen 2 standard is proposed.
The proposed system is compatible with the EPCglobal class 1 gen 2 standards, this mean that:
  The proposed tags could be inserted with conventional tags and identied by the conventional readers without affecting the performance.
  The conventional tags can also inserted with the proposed tags and could be identied by the proposed readers without affecting the performance.
Using the proposed system, the reading efficiency will be increased signicantly up to 100%.

## Slide 28
Thanks for your kind attention!
Hazem.a.elsaid@fau.de